## Slide 1: The Quantity Take-off Thread
Early Design Quantity Take-off

## Slide 2: QTO Early Design Thread
Outline
Early design
Quantity take-off
Building on the work of others
Information Delivery Manual (IDM)
Model View Definition (MVD)

## Slide 3: QTO Early Design Thread
Early Design
General model for Testbed is Integrated Project Delivery
Not defining generic or standard project phase terms
Testbed seeks to
  Define what we want to achieve with the QTO and when
  Nature of and types of information that are required to support costing
  What the design team could and should do during early design to generate quality of information needed for costing

## Slide 4: QTO Early Design Thread
Quantity Take-off
Why QTO
  Use of qualitative information to augment the quantitative information
  Interaction of modelers and estimators – transport mechanisms and the methods of exchange to communicate more seamlessly
Role of the estimator

## Slide 5: QTO Technical Overview
Quantity
Takeoff
Tool
IFC export
IFC import
file system
XXX
Schedule
Construction
Recipe
Schedule
Unit Cost
Schedule
quantity import
quantity export
BIM-Authoring
Tool
BIM 1
BIM 2
BIM N
Schedule
Web Services
QTO IFC
store
QTO
store
Notes: QTO tool:
Imports IFC
Assigns CAD quantities
Assign labor, material, equipment using industry schedules
5

## Slide 6: QTO Early Design Thread
Generic AEC/FM BIM View Description Concept Design to QTO/Cost Estimating
Design
Model
(objects, attributes)
Design
Quantities
(object quantities)
Production
Quantities (assemblies, items, resources)
this view
Based on BLIS view ‘Arch. Design >> Quantities take off / cost estimating’ (2000)
Based on SABLE DAPI ‘Quantity Information for Cost Estimation’ (2004)
Based on IAI German Speaking Chapter (GSC) adaptation for ‘Base Quantities’ (2007)
TESTBED THREAD AREA OF INTEREST

## Slide 7: QTO Early Design Thread
Generic AEC/FM BIM View Description Concept Design to QTO/Cost Estimating
Three levels of QTO information exchange agreed internationally
  QTO Level 1 – BIM objects, with geometry and definition properties, no element quantities
  QTO Level 2 – BIM objects and basic quantities that are useful internationally, but no geometry
  QTO Level 3 – BIM objects and extended quantities that require national and local calculation rules, but no geometry
QTO Thread view is QTO Level 2

## Slide 8: use case
export/upload BIM model with base quantities according to MVD
import/download BIM model (+ base quantities)
validate/aggregate quantities, define task based quantities, access catalog (of recipes/formulas)
generate bill of quantities/ export/upload to document server
<next round of refinement>
QTO Early Design Thread
BIM Authoring

## Slide 9
QTO Early Design Thread

## Slide 10: QTO Early Design Thread
IDM Overview
Goals and objectives
Focused on discrete process
Specifies
  Where a process fits and why it is relevant
  Who are the actors
  What is the information created and consumed
  How the information should be supported by software solutions
Communication document between BIM users and software providers
  User needs in plain language – perspective of the user
  Software developers know what exchanges are necessary
Leads to Model View Definition (MVD) Diagrams

## Slide 11: QTO Early Design Thread
Unique aspect for this task
Alignment with BPEA IDM
Fast track of QTO – IDM parallel effort with MVDs
IDM Components
Process Model Diagram
Exchange Requirements

## Slide 12: QTO Early Design Thread
IDM Outline
Process Model
  Overview
  Specification of process
  Specification of data objects
  Specification of coordination point gateways
Exchange requirements for QTO Input (early design)
Exchange Requirements for Quantity Take-off Output (early design)

## Slide 13: QTO Early Design Thread
Sub-process

## Slide 14: QTO Early Design Thread
Sub-process

## Slide 15: QTO Early Design Thread
Exchange Requirements
Object types and properties
IFC Model representation

## Slide 16: QTO Early Design Thread

## Slide 17: QTO Early Design Thread
Exchange Requirements Object Types
IFC system objects
Geospatial data
Properties (metadata)
Project
Site
Building
Building Story
Space
Wall
Slab
Beam
Column
Opening
Door
Window

## Slide 18: QTO Early Design Thread
Exchange Requirements Object Types
Curtain Wall
Stair Flight
Ramp Flight
Equipment
Plumbing Fixtures
HVAC System
Electrical System
Hot Water System
Cold Water System
Vertical Circulation System
Exchange Requirements Object Types
IFC system objects
Properties (metadata)

## Slide 19: QTO Early Design Thread
Example Exchanges
Prepare/Adjust BIM for QTO/Cost Estimate [1.1]
Derive Building Information
Assumes a building model with geometry is available – building layout
  Space configuration
  Outline layout of building elements
  Determine proposed positions of walls and doors
Building Object Type for Quantity Take-off
Functional classification source is OmniClass table 11 (construction entities by function)
  For the Testbed, use the IBC classifications to align with BPEA

## Slide 20: QTO Early Design Thread
Example Exchanges
Create Project Space Types [1.1.1]
Space Object Type for Quantity Take-off
The functional classification source is OmniClass table 13 (space by function)
  For the Testbed, use the GSA space types to align with BPEA
Spaces may be Interior or Exterior
  Optional source OmniClass table 14 (space by form)

## Slide 21: QTO Early Design Thread
http://www.blis-project.org/IAI-MVD/
Reference: BSA-001

## Slide 22: QTO Early Design Thread

## Slide 23: QTO Early Design Thread
Final Thoughts
Release of IDM for public comment – late January
Same Test Model as BPEA Thread

## Slide 24: QTO Technical Overview w/ XML & Web Services
Quantity
Takeoff
Tool
IFC export
IFC import
file system
XXX
Schedule
Construction
Recipe
Schedule
Unit Cost
Schedule
quantity import
quantity export
BIM-Authoring
Tool
BIM 1
BIM 2
BIM N
Schedule
Web Services
QTO IFC
store
CPD Catalog
post IFCxml
QTO
store
post IFCxml
Notes: QTO tool:
Imports IFC
Assigns CAD quantities
Assign labor, material, equipment using industry schedules
24

## Slide 25: QTO Technical Overview w/ XML & Web Services
Quantity
Takeoff
Tool
IFC export
IFC import
file system
XXX
Schedule
Construction
Recipe
Schedule
Unit Cost
Schedule
quantity import
quantity export
BIM-Authoring
Tool
BIM 1
BIM 2
BIM N
Schedule
Web Services
QTO IFC
store
Arch. CPD Catalog
post IFCxml
QTO
store
post IFCxml
QTO CPD Catalog
Notes: QTO tool:
Imports IFC
Assigns CAD quantities
Assign labor, material, equipment using industry schedules
25