# Chapter 2.3	Future Versions

## Introduction

Primarily this section of NBIMS Version 1 - Part 1 identifies what needs to be accomplished in order to issue Part 2.  Also discussed are the process and timing that will be followed to achieve that goal and to issue future versions of the Standard.  Most of this chapter is a compilation of information found and discussed in other chapters.

## Background

The NBIMS Version 1 - Part 1:  Overview, Principles, and Methodologies is intended to first introduce the reader to a comprehensive Building Information Model (BIM) and all the possibilities it will bring to the capital facilities industry.  The United States capital facilities industry is a long way from fully realizing all the opportunities of BIM and this chapter is intended to provide the roadmap that will be required for attaining the goals identified in the whole of this document.

Figure 2.3-2 identifies major activities that are enabled by the Standard.  The information presented below will discuss the tasks needed to achieve each of these high-level capabilities.

## Relevance to Users

BIM is in use today and is flourishing, but it carries many of the problems of the past.  These problems are primarily related to lack of sharing of information between lifecycle phases, since many practitioners are still only concerned with their phase of the project and fail to recognize their stewardship role in the overall lifecycle of the facility.  In order for a BIM to be fully implemented and its potential fully realized, it must allow for the flow of information from one phase to the next, from inception onward.  This can effectively only be achieved through open standards.  Today, BIM is being defined by the capabilities that a specific vendor can provide and not by the requirements that design and construction professionals or, more importantly, the operators, sustainers, and owners of a facility need.  Open standards are the only economical way all subject matter vendors can participate.  A time when one vendor will be able to provide all the tools necessary for the capital facilities industry is not foreseen and is quite unrealistic.

The reader is encouraged to read the complete NBIMS document then return to this chapter, since it identifies the roadmap to achieve full realization of the opportunities BIM provides.  It provides the timeline when users may expect certain capabilities to reach maturity.

There are many concerns on which the industry must come to a decision; many of these may require the formation of consortiums to accomplish the task.  Funding will also be required, and finding resources interested in ensuring those capabilities exist may be a challenge.  While a certain end state is desired, ensuring that all the pieces necessary to accomplish that end state may not have the level of interest needed to fund them.  However, if the foundation capabilities are not in place and are not strong, then the final product will likely be inadequate and not attain the expected potential.

## Relevance to the National BIM Standard

Accomplishing all the tasks identified in this section will be daunting and priorities are likely to change over time.  The industry will not be able to boil the ocean; therefore, the process must be broken into small doable pieces that yield usable results and benefits as quickly as possible.  With many hands working toward a common vision these tasks can be accomplished as long as the goals are clearly stated and the relationships and prerequisites well understood.  It is critical that active participation of practitioners remain high so that the final products do in fact support their requirements.

## Discussion

Our ultimate goal is to improve construction productivity in the United States and to keep us competitive internationally.  Many of the aspects of this overarching goal will be accomplished by a large consortium of players.  The area that NBIMS is focused on is the design of the theory and structure for a new way of thinking about facilities and structures as information models.  The industry is not just pushing a theory but is designing the process and structures for the information:  using objects such as Industry Foundation Classes (IFC or ifc), using information exchanges such as Information Delivery Manual (IDM), using model views such as Model View Definition (MVD), and dictionaries such as International Framework for Dictionaries (IFD) to create and sustain a BIM.

The table (Figure 2.3-1) shows a desired extension to one originally provided by the Bureau of Labor and Statistics in 2004, which showed a declining productivity rate for construction, while other segments of the economy were improving at record rates.  The NBIMS Initiative’s goal is to implement some of the same techniques, used in other industries, in the capital facilities industry to achieve the similar productivity increases and to reverse the current downward trend.  The rate of improvement will depend on how seriously the industry and the country view the crisis and come forward with the necessary resources.  It is hoped that construction productivity can at least begin to show improvement before the end of this decade and follow our projections into the future.

Figure 2.3-1  Construction Productivity (Historical information courtesy of Bureau of Labor Statistics; future projection courtesy of DKS Information Consulting, LLC.)

How soon the detailed roadmap presented below is accomplished will depend on how soon we lay the foundation needed to achieve it.  While the NIST study and others have identified the loss of billions of dollars a year from inefficient business practices, we have not been able to identify the specific sources of those dollars in order to be able to redirect them to solve the problem.  The primary reasons are that the dollars are widely distributed and that most practitioners have an accepted way of doing business such that the imbedded waste and ways to improve are not readily seen.  Hence, the industry makes small incremental improvements to inefficient processes instead of the substantive changes required that involve the entire capital facilities industry.

## Next Steps

The next steps in the NBIMS Version 1 -Part 1 are gleaned from each chapter and included here as a summary.

Supporting Tier 4

- Continued promotion of information relationships from the highest level, worldview, to the lowest level, object view, is required throughout the capital facilities industry to ensure that we maintain a continuum of information flow from the smallest to the largest pieces and vice versa. All parties involved must be supportive of the model at this level before there can be acceptance at more detailed levels. The NBIMS Initiative includes OSCRE, OGC, IAI, and many others who all need to become involved in order to reach industry wide consensus.

- A key element of success will be implementing Information Assurance procedures so those who store information in the model and those who retrieve it are assured of the accuracy and security of the information. While commonplace in the banking and personnel industries, it is still relatively new concept in the capital facilities industry. Work must be done to ensure industry wide implementation so that trust can be ensured.

Supporting Tier 3

- Research is required to evaluate the current level of capability of BIMs in use in the industry today and to continue evaluating the rankings proposed for the capability maturity model remains valid. There was concern that the bar may have been set too high for most current BIMs to be “certified” however, this proved not to be true. The chapter BIM Minimum will be revised as required over time to reflect the status of the industry.

- The Capability Maturity Model chapter has been coordinated with the BIM Minimum chapter to ensure that the certified level is in fact what is being described in that section. Many so-called BIMs in existence do not meet the NBIMS definition of a BIM, since they are really only intelligent drawings, visualization tools, or production aides. The current Capability Maturity Model gives the capital facilities industry a spectrum of tangible capabilities by which to determine the current maturity of a BIM and to provide higher levels on the spectrum as developmental goals. Future work will be done to improve the Maturity Model so that it mirrors the burgeoning BIM community.

- The governing body of NBIMS will need to certify BIMs and testing processes in order to build a database of best practices and to isolate areas of opportunity for improvements in the BIM community, as well as to provide a means and motivation for users to create reliable information that is stored in open and interoperable formats.

- The industry will need to implement Information Assurance procedures at all levels of BIM.

Supporting Tier 2

- Identify the maturity baseline in the industry as it stands today, determine the typical level of BIM in use, and validate that it meets the minimum identified in this document

- Continue developing a vision for more mature BIMs and develop a roadmap for raising the minimum BIM bar. Identify deadlines for achieving higher level and more mature implementation over the next 20 or more years.

- Implement Information Assurance procedures to support Tier 2.

- Identify existing BIM projects that qualify as candidates for inclusion in the standard (together with Scoping and Requirements Development).

- Evaluate candidates and create a plan for developing qualified candidates into a standard (together with Scoping and Requirements Development).

- Review and comment on IDM Process Maps (developed by Requirements Development).

- Review and comment on IDM Exchange Requirements (developed by Requirements Development).

- Facilitate review and feedback by software developers.

- Plan and manage a pilot implementation/use program (together with Testing).

- Incorporate lessons learned from implementations/use to update Process Map, ERs, and MVD (together with Requirements Development and Testing).

- Plan and manage the consensus process (together with Executive Committee).

Supporting Tier 1

- The IFC development work is currently being done overseas. While there are links to chapters developing IFC worldwide, there is currently very little U.S. involvement. U.S. involvement in this effort must increase in order to develop IFC that will fully meet our future needs and to remain competitive.

- Software vendors continue to support open standard IFC in their products at various speeds. Each product has varying levels of success at importing and exporting IFC due to their internal configuration. Continued focus on the benefits of the IFC based neutral file format used to communicate between products needs to be maintained. This is the basis for the NBIMS open standards approach.

- Implementing Information Assurance procedures:

  - Review the OGC GeoDRM Reference Model from the perspective of information exchanges in BIMs.

  - Identify and document use cases.

  - Make plans to participate in future OGC Interoperability Programs.

- The need for UniFormat™ harmonization, along with enhancement, and coordination of other OmniClass™ tables must continue.

- Work with and further support OSCRE efforts to link the planning, design, and construction activities to the owners, operators, investors, and tenants of facilities.

- Provide continuing education for practitioners in all aspects of the real property industry.

- Support software vendor implementation of the ontologies and taxonomies.

### Schedule

Several related documents will be produced over time in addition to and supporting the National BIM Standard.  One such document is the Generic Implementation Guidelines.  Although not a direct part of NBIMS, they will be based on NBIMS and therefore updates to NBIMS should be followed by the generic implementation guidelines.  The Generic Implementation Guidelines are the common elements that would be used by all.  Individual companies and organizations will augment the Generic Implementation Guidelines with their own unique requirements, but these should be limited in nature as they are somewhat duplicative.

It is estimated that new versions of NBIMS will be issued on the following schedule.  The Generic Implementation Guidelines should follow these documents by three to six months.

- NBIMS V1 - Part 1	December 2007

- NBIMS V1 - Part 2	July 2008

- NBIMS V2		July 2009

- NBIMS V3		July 2011

- NBIMS V4  		July 2014

A new version will be issued every three to five years after NBIMS has reached some level of dynamic equilibrium.

Industry will be solicited to participate in a consensus process for the items needing standardization identified in the section below. Those products ready for submission to the consensus process will be incorporated into the next version.  NBIMS V1 - Part 2 will include items undergoing this process.

### Items Needing Standardization

The following are items that have been identified throughout the document as needing to be standardized in future versions of NBIMS.

### Chapter 3.1  Introduction to Exchange Concepts

- More BIM packages need to incorporate NBIMS structured content so that property sets are interoperable.

### Chapter 3.2  Data Models and the Role of Interoperability

- OmniClass tables need to be accepted as standards for use in NBIMS.

- The NBIMS Hierarchical Relationship needs to be accepted as a standard.

- Completion of the work involved with NWI 241 to harmonize IFC and ISO 15926. It is anticipated that this will be coordinated through a FIATECH project.

- Consensus on the hierarchy from worldview to detailed facility or structure view. (July 2008 as part of NBIMS V1 - Part 2)

- Overall consensus on use of a procedural lifecycle roadmap for the capital facilities industry using one of the existing best practice examples as its basis. (NBIMS V2)

- Incorporation of the accepted procedural best practice into software. (NBIMS V3)

### Chapter 3.3  Storing and Sharing Information

- Information sharing strategies and standards for manufacturers and suppliers to ensure models are sustainable.

- Defining information structures related to activities included in a model.

- Defining how models will support sensor networks for real time facility operations.

- Strategies to incorporate server and web based service oriented architectures.

### Chapter 3.4  Information Assurance

- Establishment of Information Assurance procedures in new models.

- Encryption-at-rest measures shall be initiated.

- Encryption-during-transmission shall be implemented.

- Building IA procedures into the management of the entire facility lifecycle.

- Metadata concerning who entered the information into the BIM and the level of quality of that information.

### Chapter 4.1  BIM Minimum

### The minimum BIM is an outcome of the current level of standardization available; however, agreement needs to be reached as to what a minimum standard entails.

### Chapter 4.2  Capability Maturity Model

- The Capability Maturity Model will need to be accepted by the industry, whether or not it can be standardized remains in question.

- It is anticipated that the certification levels will be adjusted annually based on some established criteria. Such criterion may be based on the winners of several BIM related awards that occur annually such as the AIA TAP BIM Awards, the FIATECH CETI Awards, and others established by the industry.

### Chapter 5.1  Overview of Exchange Standard Development and Use Process

### No specific items needing standardization have been identified for this section.

### Chapter 5.2  Workgroup Formation and Requirements Definition

### No specific items needing standardization have been identified for this section.

### Chapter 5.3  User-Facing Exchange Models

- Development of ERMs for the end user processes selected for V1.  (See Chapter 5.2)

- Development of one or more generic MVDs (depending on the number of high level exchange scenarios that the ERMs span, e.g. architectural design to structural design, architectural design to HVAC design).

- Review and comment on these MVDs by industry associations and vendors.

### Chapter 5.4  Vendor-Facing Model Definition, Implementation, and Certification Testing

- Since this document is focused on defining the processes and tools by which a Version 1 National BIM Standard will be developed and NOT on the actual standard, there are no MVDs included in this document.  MVDs will be developed in future releases of the actual standards document.

- Identify existing BIM projects that qualify as candidates for inclusion in the standard (together with Scoping and Requirements Development).

- Evaluate candidates and develop a plan for developing qualified candidates into a standard (together with Scoping and Requirements Development).

- Review and comment on IDM Process Maps (developed by Requirements Development).

- Review and comment on IDM Exchange Requirements (developed by Requirements Development).

- Develop Model View Definitions (as defined in the MVD Development Process section).

- Facilitate review and feedback by software community.

- Plan and manage a pilot implementation/use program (together with Testing).

- Incorporate lessons learned from implementations/use to update Process Map, ERs, and MVD (together with Requirements Development and Testing).

- Plan and manage the consensus process (together with Executive Committee).

- Generate and publish V1 NBIMS documents (together with all committees).

### Chapter 5.5  Deployment

- Develop example Project Agreements between parties to exchanges.

- BIM creation in which certified software is used to author building information models.

- Data validation in which delivered BIM data is checked for compliance with the Project Agreement.

- BIM use in which delivered BIM data is imported and used in certified software by exchange parties to accomplish project objectives.

### Chapter 5.6  Consensus-Based Approval Methods

- The consensus process must be developed and deployed.

### Appendix A  IAI Industry Foundation Classes (IFC or ifc)

- The IFC continue to be developed and expanded and new versions will be issued. NBIMS will continue to adopt the work of the ISO and the IAI International as the IFC are incorporated into software.  IFC are at the Publicly Accepted Standard (PAS) stage (ISO/PAS 16739) and as such are not yet an ISO standard, although they are headed in that direction.

### Appendix B  CSI OmniClass™

- The fifteen OmniClass tables should be accepted as industry standards.

- Tables 11, 12, 13, 14, 22, 31, 32, 33, 34, and 41 are ready to be submitted to the consensus process in 2007.

- Table 21 is undergoing harmonization and will be ready for consensus in 2008.

- Table 23, 35, 36, and 49 will be ready at a future date.

- We will use a modification of the NIBS consensus process to incorporate these documents.

Appendix C  CSI International Framework for Dictionaries (IFDLibrary™)

### The IFDLibrary partners have a number of projects underway that are starting to address working with the IFD and integrating it with the IFC model to support interoperability.  North America is currently pursuing the following projects.

### ICC SmartCodes.  The primary project CSI is pursuing as an initial test case is supporting the International Code Council (ICC) SmartCodes project.  ICC has identified terms from the energy code and identified their relevant properties.  This work is captured in spreadsheets to develop the input tool and access to the API. With the energy code complete, we will move on to support other parts of the International Building Code.

### NBIMS.  Once the toolset and procedures are established, CSI plans to make them available to support all projects looking to achieve interoperability through using the IFC model and IDM process definitions.  Initial work with the development committee on the Product Property Sets for Specifiers project is expected to utilize the IFD to establish the requirements for specifications by project phase.

### Additional Standards Efforts

- Readers of this document who represent widely used domain standards (i.e. normative standards) are encouraged to undertake NBIMS projects to help define those information exchanges needed for their specific communities.  Readers of this document who utilize local standards are asked to participate in relevant NBIMS projects to identify the extent to which requirements defined by their standards may be represented in the NBIMS open-standards framework.

- NBIMS encourages software vendors to participate in the discussion of this methodology to provide an open framework for their interoperability projects.  Such a framework will reduce the cost of vendor participation in NBIMS and ultimately provide critically needed end user functionality that increases the ease of use of each participating software system.

## Priorities

While the above items all need to be completed in order to achieve our comprehensive BIM goals, the list below identify the most critical and specific items that can begin standardization processes or that require specific support for the consensus processes either underway or soon to be underway.  They are listed in no specific order since each should be investigated in detail to understand the level of effort that will be required to prepare them for balloting and consensus.  It is hoped that a significant portion of the list will be addressed in Part 2, but that is yet to be determined.  This will be a significant role for the consensus committee of NBIMS.

- Develop standardized Model View Definition and conduct consensus process.

- Establish standard information assurance procedures for a new model.

- Publish V1 NBIMS Model View Standard in conformance with IAI International.

- Initiate standard encryption-at-rest measures for NBIMS based products.

- Support OmniClass™ table 21 harmonization efforts to prepare for consensus.

- Implement standard encryption-during-transmission measures for NBIMS based products.

- Build standard IA procedures into the management of the entire facility lifecycle.

- Develop standard audit trail and quality indicators for BIM.

- Continue support for standard IFC development.

- Conduct consensus process to standardize the information exchange template.

- Conduct consensus process for OmniClass™ tables 11, 12, 13, 14, 22, 31, 32, 33, 34, and 41.

- Conduct consensus process for the hierarchical relationship.

- Support completion of the work involved to harmonize IFC (ISO/PAS 16739) and ISO 15926.

- Conduct consensus on use of a procedural lifecycle roadmap for the capital facilities industry using one of the existing best practice examples as a basis.

- Incorporation of the accepted procedural best practice into software.

- Conduct consensus to standardize minimum BIM.

- Conduct consensus process to make Early Design a standard part of NBIMS.

- Conduct consensus process to make COBIE a standard part of NBIMS.

# Footnotes

U.S. Department of Commerce, National Institute for Standards and Technology, “Cost Analysis of Inadequate Interoperability in the U.S. Capital Facilities Industry.”  (NIST GCR 04-867, August 2004 at http://www.bfrl.nist.gov/oae/publications/gcrs/04867.pdf.

# Text boxes

2004    2008    2012    2014    2018    2022    2024  ….

Figure 2.3-2  NBIMS Exchange Tier Architecture (Courtesy D. Davis, AEC Infosystems)

http://www.facilityinformationcouncil.org/bim/pdfs/ExchTierArch.jpg